## Slide 1
HACKYEAH 2026 · OPEN TASK: SMART CITY
Pomóc
The network that is already there
A dual-use civic mesh: neighbourhood sharing on an ordinary Tuesday, resilient communication on the day the network goes dark.
Team: Apexlab
Members: Vargha Csongor Csaba · Magyar Dániel · Fábi Tamás

## Slide 2
THE PROBLEM
Two failures, one root cause
On an ordinary day
Resources sit idle. Nobody nearby knows they exist.
~13 min
a drill is used in its whole lifetime
On the bad day
Help sits unreachable. The mobile network is the first thing to fail.
~80 m
between a cardiac arrest and the AED on the wall
The city already owns what it needs. It is in the wrong pocket.

## Slide 3
THE IDEA
One network, one identity, two rule sets
Peace mode
Borrow a drill, get sour cream next door, hand over a parking spot
Reach is hop-limited (default ~3 hops, configurable): local by protocol, not by policy
Free by default; a fee only when a lender asks one for a loan
Emergency mode
Signed official alerts, “I am OK” check-ins, life-critical requests
No operator network needed: home routers mesh over Wi-Fi, phones relay over Bluetooth LE
Fees off, priorities on, store-and-forward on
Runs on what the city already has: phones and ISP routers. Routers are the Wi-Fi mesh backbone, phones the Bluetooth edge.

## Slide 4
TARGET SCENARIO · VISION, NOT IN THE SIM
The AED, in ~90 seconds
1
Ola sends a signed LIFE_CRITICAL request with her location attached.
It floods the mesh at top priority, pre-empting everything else.
2
The mesh knows a registered AED ~40 m from Marek.
He is the nearest capable responder and accepts with one tap.
3
Everyone else sees the request is taken.
The mesh guides Marek to the AED, then to Ola.
4
Marek runs it over.
One person moves, the messages did the rest.
Messages travel hop by hop. The object travels with one person.

## Slide 5
EMERGENCY MODE
Three levels, one signed declaration
 | L1 Disruption | L2 Disaster | L3 Security
Cause | cell outage, cable cut, cyberattack | flood, storm, blackout | armed attack, hybrid threat
Entered by | automatic (no backhaul) or local authority | local authority declaration | local authority declaration
Router portal | read + check-in | read + check-in + request | read only
Citizen requests | emergency requests: life-critical, safety, “I am OK” | emergency requests: life-critical, safety, “I am OK” | life-critical, safety, “I am OK”; casualty reports sealed to the authorities
Citizen info | on | on | off (rumour control), phones go quiet
Jamming the cells can force L1 at most. Everything above it needs a signature. Portal inputs are aggregated once a minute per router, so the mesh load is bounded by routers, not attackers.

## Slide 6
PEACE MODE
Resource sharing within a few hops
Request → neighbours within the hop limit see it → first accepted match closes it
Shared-ownership amortisation: a tool lent for small fees pays itself back
Registered static resources: public AEDs, shelters, water points pinned to the map
Daily OK (opt-in senior care): no phone use for hours or a detected fall → the phone asks “Are you OK?” → the people the senior chose → only then nearest neighbours and 112
Local questions and answers: is the pharmacy open, who has a spare car seat, is the playground flooded
Guard rails: rate limits per identity, reputation, quiet hours, category mutes
Why it matters for the bad day: the app is already installed, the identities already issued, the graph already known
Example request
Cordless drill, Sunday afternoon
2 PLN fee
3 hops
expires 2 h
Matched by Marek, 2 hops away, in ~4 minutes.
No shop trip, no delivery van, one drill working instead of two idle ones.

## Slide 7
ARCHITECTURE
How the pieces fit together

## Slide 8
TRUST
Verified people, verifiable offline
Register once through the national identity wallet (mObywatel / EUDI). The key is born in the phone's secure chip and never leaves it; the Authority verifies the person and the device, then signs a citizen certificate.
Every message is signed. Any node verifies it with the Authority root key already in the app. No network needed.
Routers hold relay certificates: they carry, they can never ask. A cryptographic rule, not a policy.
Pseudonymous on the wire. ~30-day keys: the phone makes a new one and the Authority re-signs it, through the mesh when the internet is gone.
Forged alerts die. Local authorities sign declarations for their area with keys under the Authority root; alerts are signed too. Anything unverifiable is dropped at the first hop.

## Slide 9
WHAT WE BUILT AT HACKYEAH
A simulation of the protocol on a city graph
Kraków district, static router layer plus mobile phone layer, in one interactive one-pager. Deterministic, playable step by step:
1
Peace request + match
2
Flooding: hop limit, TTL, dedup
3
Cells down → L1, router backbone
4
Power down → phone-only, store-and-forward
5
L2 west, L3 east: regional declarations
6
Forged request rejected
Live metrics: reach, delivery per class, hops, latency. Set device counts and radio range and see how coverage changes with fewer nodes.
Honest scope
Built: the protocol simulation (modes, levels, flooding, hop limits, TTL, de-duplication, store-and-forward, degradation)
Not simulated: cryptography (a trust flag stands in), topology gossip, rate limits, AED registry and guidance, casualty reports, router portal, Daily OK. Timers are compressed for the demo
Not built: router firmware, identity integration, Authority services
Vision, not in the sim: coverage planning. Phone density shifts by district and over time; the city sees where Pomóc is thin and responds with relay nodes, campaigns or incentives
Pomóc is a vision; the simulation is the argument.

## Slide 10
WHY IT IS BELIEVABLE
Every piece has been tried. Nobody has combined them.
00000JAPAN and Comcast already flip existing home and public Wi-Fi open in disasters, by remote config
EUDI wallets are mandatory EU-wide: Pomóc would plug into mObywatel in Poland, DÁP in Hungary, any national wallet
Alert RCB is moving into mObywatel; Pomóc is its offline continuation when the cells are down
Japan's Relay-by-Smartphone has tested phone-to-phone message relaying since 2011
Peerby: ~80% of neighbourhood requests filled within ~30 minutes
Standard parts: 802.11s router mesh (OpenWrt), BLE / Wi-Fi Aware, TR-369, PKI with secure-element keys
The point
The first 24 hours. After an attack or disaster, authorities and emergency services need time to respond. Pomóc keeps a communication platform alive in that gap.
Aim: fewer casualties. Life-critical requests, casualty reports with voluntarily shared position, and verified official alerts keep moving without cells or power.
Already in every pocket. Almost no new hardware, no new identity scheme: phones, home routers, a few battery-backed relays and the national EUDI wallet.
No ISP payment. Government-legalised, nonprofit software. ISPs are not paid. The only cost is the gateway servers the governance has to maintain anyway as communication hubs.
Next: open protocol spec · pilot in one district with one ISP · battery-backed relay placement from the coverage model. Concept, research, docs, simulation and this deck were made with AI assistance (Claude Code; title illustration generated with Gemini); the team stands behind all of it.